## Slide 1: The Impact of Private Autonomous Vehicles on Vehicle Ownership and Unoccupied VMT Generation
Wenwen Zhang, Subhrajit Guhathakurta, Elias Khalil
January 8th, 2018
2018 TRB Conference | Washington D.C.

## Slide 2: Deployment Models of AVs
Private AVs (PAVs)
Shared AVs (SAVs)
Transit Complementary AVs (TCAVs)

## Slide 3: Existing Studies and Public Opinions
Bansal et al. (2016)
  13-35% expressed interests in SAVs
Krueger, Rashidi, & Rose (2016)
  30% may try SAVs
Haboucha, Ishaq, & Shiftan (2017)
  41% willing to participate SAV program
SAVs
CTAVs
PAVs
Burns, Jordan, & Scarborough, 2013
Spieser et al., 2014
Fagnant & Kockelman, 2014
Zhang et al., 2015
Greenblatt & Saxena, 2015
Chen, Kockelman, & Hanna, 2016
Zhang & Guhathakurta, 2017
Bansal et al., 2017
…
Chong et al., 2011
Shen et al., 2017
…
Schoettle & Sivak, 2015

## Slide 4: Research Questions
How Privately Owned AVs will change VEHICLE OWNERSHIP?
  How much reduction can be achieved?
  What type of family are more likely to benefit from AV technology and own less vehicles?
How much UNOCCUPIED VMT will be generated?
  When PAVs relocate to serve different household members

## Slide 5: Assumptions & Simplifications
No change in the travel behaviors;
The estimated VMT changes stems exclusively from the re-routing of unoccupied AVs from prior trip destination generated by another household member to the existing trip origin;
Vehicles are only shared by household members not among households;
It assumes a 100% market penetration rate and heterogeneity in the preferences for AVs are not considered.

## Slide 6: Research Framework
STEP 1 Vehicle Reduction Potential
A greedy algorithm to determine minimum number of PAVs needed to serve each household
STEP 2 VMT Minimization
A MIP optimization model to optimize vehicle routes to minimize VMT
STEP 3 Spatial Patterns
A Trip Assignment Model to determine the spatial distribution of VMT
[1] Atlanta Travel Survey 2011
[2] Synthetic Trips from ARC Activity Based Model
DATA

## Slide 7: STEP 1 Vehicle Reduction Potential A Greedy Algorithm
A Greedy Algorithm follows the problem solving heuristic of making the locally optimal choice at each stage with the hope of finding a global optimum.
Time of the day
Example Family owns 3 private conventional cars
1
12
6
7
8
17
18
19
1) Load all the vehicle trips
Origin
Destination
Departure time
Arrival time

## Slide 8: STEP 1 Vehicle Reduction Potential A Greedy Algorithm
A Greedy Algorithm follows the problem solving heuristic of making the locally optimal choice at each stage with the hope of finding a global optimum.
Time of the day
1) Load all the vehicle trips
Example Family owns 3 private conventional cars
1
12
6
7
8
17
18
19
2) Scan the trips by time of the day, add one more required vehicle if no existing vehicle can serve the trip
Required Vehicle = 0

## Slide 9: STEP 1 Vehicle Reduction Potential A Greedy Algorithm
A Greedy Algorithm follows the problem solving heuristic of making the locally optimal choice at each stage with the hope of finding a global optimum.
Time of the day
1) Load all the vehicle trips
Example Family owns 3 private conventional cars
1
12
6
7
8
17
18
19
2) Scan the trips by time of the day, add one more required vehicle if no existing vehicle can serve the trip
Required Vehicle = 0
Required Vehicle = 1
PAV Inventory
Busy = True Until Arrival Time
Location = Trip 1 Dest.

## Slide 10: STEP 1 Vehicle Reduction Potential A Greedy Algorithm
A Greedy Algorithm follows the problem solving heuristic of making the locally optimal choice at each stage with the hope of finding a global optimum.
Time of the day
1) Load all the vehicle trips
Example Family owns 3 private conventional cars
1
12
6
7
8
17
18
19
2) Scan the trips by time of the day, add one more required vehicle if no existing vehicle can serve the trip
Required Vehicle = 1
PAV Inventory
Busy = True Until Arrival Time
Location = Trip 1 Dest.
PAV Inventory
Busy = False
Location = Trip 1 Dest.

## Slide 11: STEP 1 Vehicle Reduction Potential A Greedy Algorithm
A Greedy Algorithm follows the problem solving heuristic of making the locally optimal choice at each stage with the hope of finding a global optimum.
Time of the day
1) Load all the vehicle trips
Example Family owns 3 private conventional cars
1
12
6
7
8
17
18
19
2) Scan the trips by time of the day, add one more required vehicle if no existing vehicle can serve the trip
Required Vehicle = 1
PAV Inventory
Busy = True Until Arrival Time
Location = Trip 1 Dest.
PAV Inventory
Busy = False
Location = Trip 1 Dest.
ENOUGH TIME* to relocate from trip 1 destination to current trip origin before current trip departures ??
NO: Add one PAV
YES: Don’t add
* Time from Google API, reflects congestion

## Slide 12: STEP 1 Vehicle Reduction Potential A Greedy Algorithm
A Greedy Algorithm follows the problem solving heuristic of making the locally optimal choice at each stage with the hope of finding a global optimum.
Time of the day
1) Load all the vehicle trips
Example Family owns 3 private conventional cars
1
12
6
7
8
17
18
19
2) Scan the trips by time of the day, add one more required vehicle if no existing vehicle can serve the trip
Required Vehicle = 1
PAV Inventory
Busy = True Until Arrival Time
Location = Trip 1 Dest.
PAV Inventory
Busy = True Until Arrival Time
Location = Trip 2 Dest.

## Slide 13: STEP 1 Vehicle Reduction Potential A Greedy Algorithm
A Greedy Algorithm follows the problem solving heuristic of making the locally optimal choice at each stage with the hope of finding a global optimum.
Time of the day
1) Load all the vehicle trips
Example Family owns 3 private conventional cars
1
12
6
7
8
17
18
19
2) Scan the trips by time of the day, add one more required vehicle if no existing vehicle can serve the trip
Required Vehicle = 1
PAV Inventory
Busy = True Until Arrival Time
Location = Trip 1 Dest.
PAV Inventory
Busy = True Until Arrival Time
Location = Trip 2 Dest.

## Slide 14: STEP 1 Vehicle Reduction Potential A Greedy Algorithm
A Greedy Algorithm follows the problem solving heuristic of making the locally optimal choice at each stage with the hope of finding a global optimum.
Time of the day
1) Load all the vehicle trips
Example Family owns 3 private conventional cars
1
12
6
7
8
17
18
19
2) Scan the trips by time of the day, add one more required vehicle if no existing vehicle can serve the trip
Required Vehicle = 2
PAV Inventory
Busy = True Until Arrival Time
Location = Trip 1 Dest.
PAV Inventory
Busy = …
Location …
Busy = …
Location …

## Slide 15: STEP 1 Vehicle Reduction Potential A Greedy Algorithm
A Greedy Algorithm follows the problem solving heuristic of making the locally optimal choice at each stage with the hope of finding a global optimum.
Time of the day
1) Load all the vehicle trips
Example Family owns 3 private conventional cars
1
12
6
7
8
17
18
19
2) Scan the trips by time of the day, add one more required vehicle if no existing vehicle can serve the trip
Required Vehicle = 2
PAV Inventory
Busy = True Until Arrival Time
Location = Trip 1 Dest.
PAV Inventory
Busy = …
Location …
Busy = …
Location …
3) Check Minimum Number of PAVs needed

## Slide 16: STEP 1 Vehicle Reduction Potential Applied to Atlanta Travel Survey
18.3% of the households may reduce vehicle ownership even if they maintain the current travel schedule.
9.5% vehicle ownership reduction
Logistic Regression Model

## Slide 17: STEP 1 Vehicle Reduction Potential Applied to Atlanta Travel Survey

## Slide 18: STEP 2 VMT Minimization MIP VMT Minimization Model
The vehicle route output from Greedy Algorithm may not provide optimum vehicle route solution for the family!
Time of the day
Example Family
1
12
6
7
8
17
18
19
PAV 1
PAV 2

## Slide 19: STEP 2 VMT Minimization MIP VMT Minimization Model
There are hundreds or even thousands of vehicle routes that PAVs can serve this family. How to find the optimal one efficiently?
Time of the day
Example Family
1
12
6
7
8
17
18
19
PAV 1
PAV 2

## Slide 20: STEP 2 VMT Minimization MIP VMT Minimization Model
Develop a Trip Connectivity Graph
Time of the day
Example Family, 2 required PAVs
1
12
6
7
8
17
18
19
Nodes are vehicle trips

## Slide 21: STEP 2 VMT Minimization MIP VMT Minimization Model
Develop a Trip Connectivity Graph
Time of the day
Example Family, 2 required PAVs
1
12
6
7
8
17
18
19
1) Nodes are vehicle trips
2) Edges: Connect Trips ONLY IF there is enough relocation time
3) Edge Cost = Relocation VMT
4) Edge is directed based on time
20
18
0
5
X

## Slide 22: STEP 2 VMT Minimization MIP VMT Minimization Model
Decision variable:

## Slide 23: STEP 2 VMT Minimization MIP VMT Minimization Model
Objective Function

## Slide 24: STEP 2 VMT Minimization MIP VMT Minimization Model
Model Constrains
Time of the day
Example Family, 2 required PAVs
1
12
6
7
8
17
18
19
1) For all the inbound possible relocation trips ONLY one is needed.
2) For all the outbound possible relocation trips ONLY one is needed.

## Slide 25: STEP 2 VMT Minimization MIP VMT Minimization Model
Model Constrains
Time of the day
Example Family, 2 required PAVs
1
12
6
7
8
17
18
19
3) The selected inbound and the outbound relocation trips should be served by the SAME PAV

## Slide 26: STEP 2 VMT Minimization MIP VMT Minimization Model
Model Constrains
Time of the day
Example Family, 2 required PAVs
1
12
6
7
8
17
18
19
4) Ensure there are only 2 required PAVs in the system!
2 vehicles enter the system!

## Slide 27: STEP 2 VMT Minimization MIP VMT Minimization Model
Model Constrains
Time of the day
Example Family, 2 required PAVs
1
12
6
7
8
17
18
19
4) Ensure there are only 2 required PAVs in the system!
2 vehicles leave the system!

## Slide 28: STEP 2 VMT Minimization MIP VMT Minimization Model
Model Constrains
Time of the day
Example Family, 2 required PAVs
1
12
6
7
8
17
18
19
4) Ensure there are only 2 required PAVs in the system!
2 vehicles leave the system!

## Slide 29: STEP 2 VMT Minimization MIP VMT Minimization Model
Objective Function
Subject to
[1]
[2]
[3]
[4]
[5]
[6]

## Slide 30: STEP 2 VMT Minimization Applied to ARC Travel Survey
Households, on average, will produce 29.8 more VMT per day per reduced vehicle.
The total VMT generation in the metropolitan area will rise by 13.3%
Chart: Excessive VMT Generation per Household
| 0-10 | 10-20 | 20-30 | 30-40 | 40-50 | 50-60 | 60-70 | 70-80 | 80-90 | 90-100 | 100-110 | 110-120 | 120-130 | 130-140 | 140-150 | 150-160
 | 53311.0386 | 64729.8924 | 52960.6025 | 41635.6461 | 30013.5961 | 22526.0936 | 14821.112 | 10784.0464 | 4204.5404 | 3923.1097 | 1045.4383 | 1174.5762 | 1847.9722

## Slide 31: STEP 2 VMT Minimization Applied to ARC Travel Survey

## Slide 32: STEP 3 Spatial Distribution Trip Assignment Model
Applied the previous 2 steps to ARC synthesized trips
  Travel survey doesn’t have all OD pairs
Generate relocation trip OD matrix
Combine relocation trip OD matrix with Existing trip OD matrix
Run Trip Assignment in CUBE

## Slide 33: STEP 3 Spatial Distribution V/C Ratio Changes by Road Type and Time of the Day
Chart: V/C Ratio
| Interstate / Freeway | Expressway | Parkway | Principal Arterial | Minor Arterial
BAU | 0.297 | 0.171 | 0.169 | 0.124 | 0.098
AV | 0.298 | 0.172 | 0.169 | 0.125 | 0.099

BAU | 0.65 | 0.514 | 0.549 | 0.468 | 0.375
AV | 0.669 | 0.539 | 0.564 | 0.486 | 0.403

BAU | 0.503 | 0.404 | 0.367 | 0.353 | 0.28
AV | 0.516 | 0.421 | 0.383 | 0.37 | 0.305

BAU | 0.692 | 0.557 | 0.554 | 0.547 | 0.44
AV | 0.709 | 0.581 | 0.576 | 0.573 | 0.479

2.4-3.0%
4.3-5.0%
2.8-4.0%
3.7-4.9%
7.5-9.2%
Increase by

## Slide 34: STEP 3 Spatial Distribution V/C Ratio Changes by Area Types
Chart: V/C Ratios
| CBD | Urban Commercial | Urban Residential | Suburban Commercial | Suburban Residential | Exurban | Rural
BAU | 0.104 | 0.105 | 0.104 | 0.1 | 0.092 | 0.075 | 0.063
AV | 0.105 | 0.106 | 0.105 | 0.101 | 0.093 | 0.076 | 0.064

BAU | 0.398 | 0.417 | 0.411 | 0.376 | 0.337 | 0.234 | 0.165
AV | 0.415 | 0.446 | 0.439 | 0.406 | 0.367 | 0.253 | 0.177

BAU | 0.368 | 0.358 | 0.334 | 0.297 | 0.255 | 0.166 | 0.124
AV | 0.391 | 0.392 | 0.362 | 0.326 | 0.283 | 0.183 | 0.135

BAU | 0.473 | 0.493 | 0.484 | 0.443 | 0.4 | 0.281 | 0.201
AV | 0.503 | 0.54 | 0.523 | 0.486 | 0.441 | 0.307 | 0.217

4.3-6.5%
7-9.4%
6.8-8.4%
8-9.9%
8.9-10.7%
8.2-10.4%
8-9.8%

## Slide 35: STEP 3 Spatial Distribution Intra-zonal relocation trips
Mostly observed during midday and evening peak hours
Midday: Concentrate in commercial TAZs
Evening Peak: Sprawl into mixed and residential TAZs

## Slide 36: Discussions and Conclusions
18.3% of the households may reduce vehicle ownership even if they follow current travel patterns; 9.5% vehicle ownership reduction
Households, on average, will produce 29.8 more VMT per day per reduced vehicle; The VMT generation in the metropolitan area will rise by 13.3%
Impact on transportation infrastructure is NOT evenly distributed
  Suburban and rural areas
  Minor and local roads

## Slide 37
Thank You
Questions & Comments